## Slide 1: Mechanical & Chemical Bonding
James G. Byrne

## Slide 2: What is Bonding?
-Join or to be joined securely to something else
Join or to be joined by a chemical bond
Jargon- special words used by particular professional or group and are difficult for others to understand.
  Fasten
  Affix
  Attach
  Fuse
  Bind

## Slide 3: Types:
Mechanical Fasteners
-Nails
-Screws/Bolts/Nuts
-Rivets
Chemical
-Glue
-Adhesive
-Epoxy

## Slide 4: Mechanical Fasteners
Nails
Faster
Cheaper
Non-Reusable
Pull-out but can be knocked back in
Screws
Slow
More expensive
Reusable
Stronger
Rivets
Slower
Expensive
Non-Reusable
Special Tool Required
Tool is bulky to fit in hard to reach locations
If damaged have to be drilled out and replaced. No quick fix

## Slide 5: Why Choose a Chemical Bond
    Stronger, safer, easier to clean up and less expensive than polyurethane glues.
    Allows eight minutes of open time and has an application temperature as low as 47 degrees F.
    One hour clamp time!
    Cleans up with water.
    Does not foam.
    Superior waterproof

## Slide 6: Types of Glue and their uses
Glue Stick-
Elmers Glue-
Wood Glue-
Hot Glue-
Crazy Glue-

## Slide 7: Why to use Yellow Glue
    Stronger, safer, easier to clean up and less expensive than polyurethane glues.(gorilla glue)
    Allows five (5) minutes of open time and has an application temperature as low as 47 degrees F.
    Less hours for clamp time!
    Cleans up with water.
    Does not foam.
    Water-resistant when dried

## Slide 8: Chemical Bonds
Yellow glue (aliphatic resin or carpenters' glue):
Aliphatic resin glue is a yellow liquid, usually sold in plastic squeeze bottles and often labeled as carpenters' glue.
Yellow glue is very similar to white glue but forms a slightly stronger bond.
It is also slightly more water resistant than white glue.
Clamping is required for about 30 minutes until the glue sets; curing time is 12 to 18 hours.
Yellow glue dries clear but does not accept wood stains.

## Slide 9: Gluing Issues
inconsistent glue coverage.
different wood species absorb glue at different rates.
varying absorption rates.
Hardwoods and softwoods will require different amounts of glue

## Slide 10: Chemical reaction
Adhesives have to stick to itself but it also have to stick to the matertials
cohesive forces- Sticks to itself. Water droplets on window form bigger droplet
adhesive forces- Adhere to an object. Water droplet sticking to window

## Slide 11: Testing the strength of the Bond

## Slide 12: Clamping Techniques
Bar Clamps
  Apply pressure to the surfaces with create a tight seal between the two boards being bonded
Wooden screw clamps:
Heavy objects:
  5 gallon water buckets
  Sand Bags
  Textbooks

## Slide 13
Wood-Joints

## Slide 15
Sample Glue Breaking force
1 Gorilla, gapped 15
2 Gorilla, no gap 230
  yellow, gapped 210
    4. yellow, no gap 190
5 Gorilla, no gap 205
6 yellow, no gap 180
7 yellow, gapped 200
8 Gorilla, gapped 15
9 Gorilla, no gap 225