## Slide 1: Electrical
Do Now:
Describe:
Voltage
Amps
Resistance

## Slide 2: Types of electricity
Static:
Alternating Current
Direct Current

## Slide 3: Electrical Components
Switch
2 way/3 way/ 4way
Load/Line Terminals
Outlet
Junction Box
Wires
Fuse
Circuit Breaker

## Slide 4: Switch Terminal layout
2 way: 3Way

## Slide 5: Types of Circuits
Series Circuit
  _______________ Path for electricity to flow.
  Voltage shared between components.
  Current is the same all points.
    Example: Christmas lights
  Diagram:

## Slide 6
Parallel Circuit
  ________________ Paths for electricity to flow
  Example: Menorah
  Voltage loss equal across each component
  Current is shared between each branch.
  Diagram

## Slide 7: Vocab
Underwriters-(UL) Product tested & meets minimum safety standards
Fire Underwriters- Tested & Inspected by to meet safety codes
Codes- Set of rules National Electric Code (NEC)
Some Codes- All bathroom and Kitchen Circuits will be protected by GFI

## Slide 8: Codes Con’t
All bathroom and kitchen circuits must be protected by a GFI.
  GFI= ___________ __________ ___________
  How does a GFI work?

## Slide 9
  #14-2 gauge wire 15 amp breaker
  #12-2 gauge wire 20 Amp breaker
  #10 gauge wire 30 amp breaker
  #8 gauge wire 40 amp breaker