## Slide 1
Footing and Foundation:
What is a footing?
A footing is made of cement and is designed to spread out live and dead loads.
Why do we need a footing?
It stops the building from sinking and/or settling into the ground. Building will be lopsided
Leaning tower of _________________

## Slide 2
What do you do when you are stuck in the sand?
  Deflate the tires to get a wider tread pattern which will stop you from sinking into the sand
  RACECAR make the track width left to right the widest possible
Anyone go OFF-ROADING?

## Slide 3: Footing Dimensions
The footing on most homes is 8” x 16” Standard Size.
8”
16”
Footing
Keyway
1” x 2”

## Slide 4: Pier:
Similar to a footing due to load bearing abilities
  Who has a basement?
    ARE THERE COLUMS IN THE ROOM
    PIERS SUPPORT THE LOAD WHERE THE FOUNDATION Is NOT DIRECTLY UNDER THE STRUCTURE
    BASEMENT IN THE CENTER
    DECKS OUTSIDE

## Slide 5: PIER DIMENSIONS
PIERS MEASURE
8” X 2’ X 2’
Notice it is the same height as the Footing
8”
2’

## Slide 6
Cement Structure the house or building is attached too.
Foundation
If you have a basement, the cement wall you see is the foundation.
How do we attach the wooden structure to a cement structure?
Construction working use a ANCHOR bolt to attach the two pieces together
ANCHOR BOLT Is 3/8” x 6”

## Slide 7
Foundation Dimensions
3’
8”
Notice: Foundation wall thickness is related to the thickness of the footing
Foundation is 8” wide
Footing is 8” Tall and 16” wide

## Slide 8
Basement floor
Solid slab no basement
Garage Floor
  Minimum 4” thick
  On top of Footing and Piers
  Does Concrete expand and contract?
    Porous water is absorbed and can freeze and crack the cement
Cement Slab

## Slide 9
Cement Slab
Cement Slab
Expansion Joint

## Slide 10
Foundation
System
½’ x 4”
Lally
Column
4” Dia Hollow

## Slide 11
Sill Sealer: Cement does not lay completely smooth. Sill Sealer Foam fills the voids
Termite Shield:
Keeps termites from destroying your structure