## Slide 1
Speed Square

## Slide 2: What is it?
Names:
  Speed Square
  Rafter Square
  Triangle Square
Materials
  Aluminum
  Steel
  Plastic

## Slide 3: Measurements
Quickly mark 90 degree angles
  Hence the name Square
Miter Cut 45 degree angles
Protractor: all angles between 0-90 degrees
Rafter Pitch Gauge
Scribe Bar
  Used to measure 1/4 “ intervals down the length if the board

## Slide 4: Activities:
Each student will have a 12” long 2 X 6 piece of lumber
Label 1 side “A” other side “B”
Side “A”
  Measure in 3 inches and scribe a line parallel to the end grain
  Measure 4 inches perpendicular to the edge grain
  Draw a diagonal from the top right corner to the lower left corner.
  What is the measurement of the diagonal?

## Slide 5: How to scribe a line:
Place foot of speed square against the edge of the board locate measurement on scribe notch and run square along the edge of the board.
  Measure ½” in and scribe a 2 inch long line, 1 inch in from the edge of the board, starting at the leg of the drawn triangle.
    Mark 1” dimension with arrows between the line and edge grain
  Measure 2” from the edge of the board and draw a 3” long line
    Mark the dimensions of the line on the board.
  Using the pivot location draw out the 15,30,45,60,75 Degree angles ¾ space between.
  Draw a 45 degree angle using both methods on top of each other.
  Draw a 90 line off of the 45 degree line using the diamond cut out.

## Slide 6: Side “B”
Lay out a rafter
Tail cut
Ridge cut
Birds mouth cut multiple times